## Slide 1: Bridge Networks
EEE Lecture-11

## Slide 2: 8.11 Bridge Networks
The bridge network may appear in one of the three forms.

## Slide 3: 8.11 Bridge Networks
For the purposes of investigation, let us examine the network of Fig. 8.64 using mesh and nodal analysis.

## Slide 4: 8.11 Bridge Networks

## Slide 5: 8.11 Bridge Networks

## Slide 6: 8.11 Bridge Networks

## Slide 7: 8.11 Bridge Networks

## Slide 10: Wheatstone Bridge
The Wheatstone Bridge was originally developed by Charles Wheatstone to measure unknown resistance values.
The Wheatstone Bridge circuit is nothing more than two simple series-parallel arrangements of resistances connected in a bridge network.

## Slide 11: Wheatstone Bridge Circuit
R1 and R2, have fixed values, and R3 is a variable resistor.
What would be the value of unknown resistance RX?
If we connected a voltmeter or ammeter between points C and D, and then varied resistor, R3 until the meters read zero, would result in the two arms being balanced and the value of RX which is equal to
Rx = R2.R3 = R4
R1
Since when bridge circuit is balanced.

## Slide 12: 8.12
Circuit configurations are often encountered in which the resistors do not appear to be in series or parallel.
Under these conditions, it may be necessary to convert the circuit from one form to another to solve for any unknown quantities.

## Slide 13
Two circuit configurations that often account for these difficulties are the wye (Y) and delta (Δ) configurations.
They are also referred to as tee (T) and pi (Π), configurations are indicated in Fig (b).

## Slide 14
It is our purpose to find some expression for R1, R2, and R3 in terms of RA, RB, and RC , and vice versa, that will ensure that the resistance between any two terminals of the Y configuration will be the same with the configuration inserted in place of the ∆ configuration (and vice versa).
If the two circuits are to be equivalent, the total resistance between any two terminals must be the same.

## Slide 24
Thank You